## Slide 1
Shower Control Box
Joystick
Digital Display
Status LED
Humidity Sensor
WiFi REST API
Receive Box
Active Buzzer
Digital Display
Status LED
Water Sensor
Motor
*x
The Cloud
Messenger Service
Temperature Sensor

## Slide 2
Increase timer on display
Start
Joystick
Up
Send message to all receiver nodes with selected time
Decrease timer on display
Down
Enter
Start timer countdown
Washing machine running?
Use API to query washing machine
Use API to pause machine
Yes
No
Dish
washer running?
Use API to query Dishwasher
Use API to pause machine
Yes
No
Timer finished?
Reset Timer
No
Yes
Control
box flowchart
Message API to Messenger

## Slide 3
Start (REST API received)
Set the display to the time received by the request
Start the countdown timer
Buzzer
Water sensor wet?
Yes
Timer finished?
No
Activate the buzzer for a short burst
Turn LED on
Wait 0.5 sec
Turn LED off
Wait 0.5 sec
Timer Finished?
No
Stop
Yes
Receiver
Flowchart
Move motor to restrict water flow from tap
Move motor to allow full water flow from tap

## Slide 4: Before: Original Diagrams
After: Revised Diagrams

## Slide 5
Shower Control Box
Number Pad
Digital Display
Status LED
Humidity Sensor
WiFi REST API
Receive Box
Active Buzzer
8*8 LED Display
Status LED
7 Digit Display
Motion Sensor
*x
The Cloud
Messenger Service
Temperature Sensor
Confirm / Cancel Button
7 Digit Display Controller
Raspberry Pi 0w
Arduino Uno
7 Digit Display

## Slide 6
“Confirm” button pressed?
Set timer to 0
Yes
Start
Number Pressed?
Send message to all receiver nodes with selected time
Append Number to display
Yes
No
Start timer countdown
Washing machine running?
Use API to query washing machine
Use API to pause machine
Yes
No
Dish
washer running?
Use API to query Dishwasher
Use API to pause machine
Yes
No
Timer finished?
Reset Timer
No
Yes
Control
box flowchart
Message API to Messenger
Back
Button Pressed?
Yes
Remove last digit
“Confirm” Button Pressed?
Yes
No
Flash LED to Acknowledge confirmation
Spike in Temp or Humidity?
Assume shower started!
No
Yes
Record temp and humidity
Set time to 15 mins
Is there a number to remove?
Send “Cancel Shower” message to all receive nodes

## Slide 7
Start (REST API received)
Set display to show “Shower Running”
Start the countdown timer
Buzzer
Motion Detected?
Yes
Timer finished?
No
Activate the buzzer for a short burst
Turn LED on
Wait 0.5 sec
Turn LED off
Wait 0.5 sec
Timer Finished?
No
Stop
Yes
Receiver
Flowchart
Wait until message finished displaying
Write “STOP” to screen
Motion Detected?
Write “Shower Running” to screen
No
Yes
Timer Finished?
No
Yes

## Slide 8
Hazard | Risk | Likelihood | Prevention
Water Restriction | Emergency access to water restricted | Low | Water flow cannot be restricted at any time for any reason. In the event of a fire it would be harder to access water.
Electricity in bathroom | Electrocution | Very Low | Any electrical appliance in the bathroom should be low voltage and battery powered and well insulated
Flashing LEDs | Epileptic Seizure | Low | Warning to anyone who might use the system

## Slide 9: Receive
No!
Shower Blame™
Still no!
The system that will beep at you when I’m having a shower
14:56
Shower Blame™
Because it mildly annoys me

## Slide 10
Ingredients
1* RaspberryPi0W
1* LCD
1* Breadboard
1* Potentialom potenti potentiometer
1* LED
1*Temp + Humidity Sensor
1* Numerical Input pad
Blutak
Receive Ingredients
2* RaspberryPi0W
1* LED 8*8 Grid
2* Breadboard
1* Active Buzzer
1* LED
1* Motion Sensor
1* Arduino Uno
1* 3D printed holder
1* 7 Segment Display
1* So many cables